Preduzeće za proizvodnju, trgovinu na veliko i malo, EXPORT-IMPORT i pružanje usluga “VATROSTAL-SIVČEV BILJANA I ORTAK” o.d. Kikinda, Rade Trnića 139, Fax/0230/424-614, Tel/ 0230/424-613 ,tl 0230/402-350, 063/8032114 ,063/8570938

e-mail: vatrostal@yahoo.com, website: www.vatrostal.rs

NAPRTNJAČA BACK PACK PUMP

Uputstvo za upotrebu                                                                                     How to use

| NAMENA Naprtnjača V 25 prvenstveno je namenjena za gašenje šumskih požara, a takođe i za gašenje početnih požara klase A i B kao što su: papir, drvo, slama, biljke, tekstil, plastika,zapaljive tečnosti I sl. |  | PURPOSE Back pack Pump (knapsack) V 25 is, in the first place, assigned for extinguishing forest fires, but also for initial fires Class A i B. such as: paper, wood, straw, plants, textile, plastic, flammable liquids etc. |
| --- | --- | --- |
| NIJE ZA GAŠENJE POŽARA E KLASE (električnih uređaja) TEČNOST IZ NAPRTNJAČE NIJE ZA LJUDSKU UPOTREBU | NOT SUITABLE FOR EXTINGUISHING CLASS E FIRES (electrical equipment) LIQUID FROM BACK PACK PUMPS (knapsack) IS NOT FOR HUMAN USAGE |
| TEHNIČKI PODACI Vreme neprekidnog pražnjenja 5 min Domet mlaza 6 m Punjenje vode max. 25 l Težina posude naprtnjače 1,5 kg Težina pumpe naprtnjače 0,6 kg Temperaturne primene 5°C do 60°C | TECHNICAL DATA Discharge time 5 min Range of jet 6 m Maximum charge of water 25 l Weight of vessel 1,5 kg Weight of pump 0,5 kg Range of usage 5°C to 60°C |
| RUKOVANJE U posudu sipati vodu i penilo u odnosu prema specifikaciji proizvođača penila. Pumpu sa crevom priključka i spojke priključiti na naprtnjaču (time je tečnost iz naprtnjače puštena u pumpu). Pumpu izvaditi iz leđnih držača ili iskopčati iz vešalice. Istezanjem i zatezanjem pumpe aktivirati naprtnjaču. Posle upotrebe OBAVEZNO isprati naprtnjaču čistom vodom. | HANDLING Pour water and foam extract in a ratio specified by foam manufacturer. The pump with its hose should be connected to the back pack through the plug and coupling, thus releasing the liquid into the pump. The pump should be removed from the back holders or released from the hanger. Activating the backpack is done by pushing and pulling the pump. After use necessarily rinse back pack with clear water. |